## Slide 1: ECDIS LAZOU EVGENIA ALEXANDROS PLAGIANNAKOS

## Slide 2: ECDIS LAZOU EVGENIA ALEXANDROS PLAGIANNAKOS

## Slide 3: PRESENTATION OF Electronic Chart Display and Information System (ECDIS)

## Slide 4
Definition: An Electronic Chart Display and Information System (ECDIS) is a geographic Information System used for nautical navigation that complies with International Maritime Organization (IMO) regulations as an alternative to Paper nautical charts. IMO refers to similar systems not meeting the regulations as Electronic Chart Systems (ECDIS).

## Slide 5: Introduction: This chapter will begin by explaining what an ECDIS is, including its history and development and what it does. The introduction will then also explain the benefits and potential disadvantages of the ECDIS and will cover the concept and importance of developing an ECDIS mindset.

## Slide 6: What is an ECS?
Electronical Chart System (ECS) is a term for all electronic equipment that is able to display a ship’s position on a chart image. The term covers a wide range of capabilities and even a smart phone can be an ECS.

## Slide 7: History and Development
YEAR | RESOLUTION | CONTENT
November 1995 | IMO Resolution A.817(19) | ECDIS “can be accepted as complying with the up-to-date chart required by regulation V/20 of the 1974 SOLAS Convention.
July 2005 | Amendments to SOLAS V | Specific reference to ECDIS statement, that it “may be used to fulfill the chart carriage requirements of regulation 19”
December 2006 | IMO Resolution MSC.232(82) | Adoption of the revised performance standards for ECDIS
June 2009 | Amendment to SOLAS chapter v/19 | Mandatory ECDIS carriage requirements
June 2010 | Manila Amendments to STCW | ECDIS competence mandatory for navigational Officers and Masters as from 01/2012

## Slide 8: ECDIS – a Complex Navigation Tool
ECDIS is a highly complex and sophisticated system, which besides the navigational functions includes components of a computer-based information system delivering a real-time display of the navigator’s own vessel located with reference to the surrounding sea area.

## Slide 9: ECDIS Display

## Slide 10
The Potential Benefits of ECDIS
• Reduced workload for the navigator (charts and nautical publications updating, voyage planning, all information in “one hand”) • Navigation in real time increasing situational awareness in combination with proper lookout • Automatic route monitoring (warnings and indications of hazards to the operator, in time arrivals) • Automatic track control (reduces bunker costs), if ECDIS is connected to the autopilot • Prediction of special maneuvers (predicted path, trial maneuvers, docking mode) • Availability of a chart during the night without night vision loss • Access to additional information resources

## Slide 11
Potential Disadvantages of ECDIS
• Too much information on the screen may cause clutter and can be distracting • Submenus can be very complex • The size of chart displayed on the screen monitor is very much reduced compared with the paper chart • Some symbols may be misinterpreted due to unfamiliarity • Automatic plotting of position can lead to complacency concerning the vessel’s position and proximity to dangers. • Confusion with ECS, unauthorized use for primary navigation

## Slide 12: The ECDIS Mindset
ECDIS is going to become the essential tool for the watch keeping officer. One could say it is even the most complex system on the bridge and although all type-approved versions fulfill the performance specifications, there are large differences between the different manufacturers’ equipment. What the officer has to develop is an ECDIS mindset. This means the attitude towards the ECDIS equipment.

## Slide 13: QUESTIONS?????

## Slide 14: QUESTIONS?????