## Slide 1
UNIVERSITY OF THESSALY
DEPARTMENT OF COMPUTER SCIENCE
Informatics of Maritime
Koukaras Theocharis (Μ012017055)
Maggaras Ivos (Μ012017077)

## Slide 2: Electronic Chart Display and Information System ECDIS

## Slide 3: What is ECDIS
Electronic Chart Display and Information System (ECDIS) means a navigation information system which, with adequate back up arrangements, can be accepted as complying with the up-to-date chart required by regulation V/19 & V/27 of the 1974 SOLAS Convention, by displaying selected information from navigation sensors to assist the mariner in route planning and route monitoring, and by displaying additional navigation-related information if required

## Slide 4: History
1986 the International Maritime Organization (IMO) and IHO (International Hydrographic Organization) agreed to set up a working group to develop an electronic chart system containing cartographic and geographic data and other information. This system was called ECDIS (Electronic Chart Display Information System). In 1989 the Canadian hydrographic service presented the first electronic map on a Norwegian ship, who had a test trip, and in 1992 the ECDIS navigation information library was presented at the Hamburg Naval Academy.
1995, IMO and IHO at the 19th Assembly adopted Decision A.817 to amend Chapter 5 of SOLAS Regulation 20 of 1974. This Decision lists the standards with which an ECDIS electronic chart system should agree in order to be recognized as an official maritime aid and an equivalent of nautical maps.
September 1997, the International Electro technical Committee (IEC) completed the final wording of international standards, which is the basis for the method of approval or certification of an IMO-compliant ECDIS valid from 30 March 1998 (Draft IEC 61174).
December 1998, the Maritime Safety Committee -MSC) adopted amendments to the implementation of the ECDIS standards to include the RCDS .
Mandatory installation of ECDIS in specific types and sizes ships start in July 2012 and are expected to be completed in all existing new ships by 2018 according to the following figure.

## Slide 6: Basic ECDIS technical and functional specifications
According to the IMO's decisions, the ECDIS system, in order to be legally and functionally equivalent, must meet the following stringent technical and operational specifications of various international organizations and committees, such as:
The Electronic Navigation Charts (ENC) must have been constructed in accordance with S-57 specifications of the International Hydrographic Organization (IHO) and have been certified by an official Hydrographic Service.
The graphical display on the ECDIS screen is in accordance with the specifications (S-52 standard) of the International Hydrographic Organization (IHO).
To meet the minimum requirements of the ECDIS functional specifications in accordance with the relevant IMO decisions.
Certification of suitability for shipboard installation according to control procedures (IEC 61174) of the International Electro-technical Commission (IEC).

## Slide 7: The basic of an ECDIS system consists of
Marinized PC.
Display.
Floppy Drive.
CD-ROM drives (chart readers & corrections).
Operating system.
Serial and digital interface (Ethernet) for optional station Nav Planning Station.

## Slide 8: ECDIS interface with other navigation systems
ECDIS can be linked to other systems such as: compass, autopilot, roller, sounder, INMARSAT terminal, automatic system location / identity indication, LORAN-C positioning system, GPS, DGPS, GNSS, GLONASS, RADAR, ARPA, wind vane, water surface, current information, ice information, NAVTEX, EGC, etc.
According to IMO standards, an ECDIS system must be connected to the positioning system of a ship, a cycle-compass and a speed and distance measuring device. For ships that do not have a cycle-compass, the ECDIS must be connected to a marine signal transmitter.
ECDIS can be either stand-alone or embedded in a console.

## Slide 9: Display cartographic and shipping data on ECDIS
According to the IMO specifications in ECDIS systems the user must have the ability to depict the elements of electronic nautical charts in the following ways:
Basic Display
- The basic display includes the following information:
- Coastline.
- Isolated security (selected by the user among the isobases contained on the ECDIS electronic nautical maps).
- Indications of individual underwater hazards with depths less than isobaths security levels within the safety margin.
- Indications of individual superficial risks and other information to be provided to be taken into account when designing and monitoring the trip and are within safety barriers such as: bridges, overhead cables,light bulbs, etc.
- Maritime traffic systems.
- Scale and distance displays, such as a linear range of distances.

## Slide 10: Display cartographic and shipping data on ECDIS
According to the IMO specifications in ECDIS systems the user must have the ability to depict the elements of electronic nautical charts in the following ways:
Standard display / default display.
The standard/default display includes all the status information from "basic display“ and in addition the following markings and indications:
- Maritime markings of lamps, wrecks, indicator lights alignment points, etc.
- Channel boundaries, floating diodes,
- Ferry routes.
- Clear areas and radar coverage areas.
- Prohibited areas and areas subject to restrictions (firing fields, submarine training areas, etc.).
- Map scale change limits.
- Indicators of measuring units of depths and altitudes.

## Slide 11: Display cartographic and shipping data on ECDIS
According to the IMO specifications in ECDIS systems the user must have the ability to depict the elements of electronic nautical charts in the following ways:
Other information.
The information in this category must include at least the following:
- Individual depths.
- Description of individual risks.
- Description of shipping markings.
- Warning notes recorded by the user.
- Date of electronic nautical map.
- Geodetic reference system.
- Magnetic divergence.

## Slide 12: Display cartographic and shipping data on ECDIS
The cartographic symbols displayed on the ECDIS screen are not contained in the digital files of ENCs. These are display in screen by selecting from a set of standard cartographic symbols (Presentation Library) of the ECDIS shipping software.
The graphical representation of the objects that make up the ENC (lights, shipwrecks, underwater cables, ducts, boundaries of restricted areas, etc.) is done with the help of application software with which:
- Select the data (ENCs) to be displayed on the screen.
- The spatial and descriptive objects are analyzed and combined.
According to the values ​​of their descriptive attributes, their objects ENC are represented with the corresponding symbol library cartographic symbols.

## Slide 13: Display cartographic and shipping data on ECDIS
The symbol library contains two different symbol categories, which are as follows:
- Traditionally symbols which are similar to the symbols of printed seafarers
Maps. (picture a)
-Simplified symbols with simple geometric shapes (picture b)

## Slide 14: Backup ECDIS security system
In addition to the technical and functional specifications of the ECDIS system, the specifications of the IMO provide for backup security procedures to ensure safe navigation in the event of failure or malfunction of the basic system. A complete system ECDIS includes, in addition to the main ECDIS, a backup system to which it must preventive transfer of the components of the normal ECDIS system to the backup security system.

## Slide 15: Electronic Navigational Charts - ENC
ENCs are vector charts that conform to the requirements for the chart databases for ECDIS, with standardized content, structure and format, issued for use with ECDIS on the authority of government authorized hydrographic offices. ENCs are vector charts that also conform to International Hydrographic Organization (IHO) specifications stated in IHO Publication S-57.
ENCs contain all the chart information necessary for safe navigation, and may contain supplementary information in addition to that contained in the paper chart. Systems using ENC charts can be programmed to give warning of impending danger in relation to the vessel's position and movement. ECDIS systems must be certified according to IMO regulations.

## Slide 16: Electronic Navigational Charts - ENC
The Maps and hydrographic data of electronic navigational charts are divided into two main structures: Raster format and vector-based structure (vector format):

## Slide 17: Electronic Navigational Charts - ENC
.
In accordance with the technical specifications of the standard S-57 of the IMO, depending on the shipping for its intended use, electronic shipping maps ENCs are classified under the following 6 categories of use:
Category 1 Overview
Category 2 General
Category 3 Coastal
Category 4 Approach
Category 5 Harbor
Category 6 Berthing

## Slide 18: Design and execution of the voyage with ECDIS
In accordance with the functional specifications of the ECDIS systems, the system provides the following possibilities for performing the basic operations and procedures of classical shipping:
1) Read the geographical coordinates of any point of electronic map (simply by positioning the cursor at that point).
2) Record the position of a point on the online map with the geographical position of the [by entering the corresponding values (F, L).
3) Measuring distance of a point from another
4) Position determination with design lines which correspond to optical bearing and measured with the radar distances.
5) Design bearings - safety distances.
6) Design polygon areas.
7) Limit areas.
8) Indication of hand-written notes on the map.

## Slide 19: Design and execution of the voyage with ECDIS
In the ECDIS the route design for the voyage from a point of departure (port of departure) until a final destination point (port of arrival) is carried out with the determination of successive points voyage, which correspond to the shift points for beam shaped ribs.
The voyage symbolized usually with the characters WP and a serial number e.g. WP1, WP2, WP3, etc.)
During the design of a route in the ECDIS is created and recorded in the database SENC, a digital file with all the essential elements of the path for easy future use, such as for the design of new routes and for the safe operation of the voyage. The digital files with the elements of the proposed routes in the database SENC, with names specified by the user, e.g. Route1 etc

## Slide 20: Design and execution of the voyage with ECDIS
The basic elements of a route of Database SENC, is:
1. The coordinates of the voyage.
2. Turn points tongue in each leg of the journey before the next change of course be determined by the designer of the voyage depending on the elements of the vessel for the speed to be observed during the voyage.
3. The safety limits route voyage CTD (Cross Track Distance), which shall be determined by the maximum allowable during the voyage deviation of the position of the ship from the planned route. This variation is determined by the designer the voyage depending on the specific shipping conditions of each region and on some systems it is possible to define:
(A) Different maximum allowable deviation for each leg of the journey.
(B) Different maximum allowable deviation on both sides of each leg of the journey.
4. Some safety parameters, which are recorded by the user, for the verification and validation of the service, as the depth of security for the voyage over shallow, the amount of the security for the voyage under a bridge and the safety distance from critical to safety of the voyage.
5. The distances between successive points voyage (these figures are calculated automatically by the system software).
6. The total distance of the planned route from the start point to the end point of the voyage, and the duration of the voyage depending on the speed to be complied with

## Slide 21: Design and execution of the voyage with ECDIS
In the diagram above shows an example of the voyage of a route in the SENC.

## Slide 22: Design and execution of the voyage with ECDIS
The digital files of the SENC of the designed routes provide to the sailor great flexibility and comfort because it is possible:
• The appearance of the whole or part of the active route in any imaging system monitor online map.
• The use of the route designed for a particular voyage, for the execution of the same voyage at a later time.
• The transfer of routes, which are entered in the database Email Map SENC in another spare ECDIS.
In the ECDIS the use of voyage and the legs of one or more routes to create a new route shall be:
• Move the different points on the voyage,
• The Delete existing points of the voyage,
• The addition of new voyage.

## Slide 24: Recording and retrieval of data recorders in the ECDIS
Another important function of the ECDIS is the retrieve recorded data of the voyage. In accordance with the requirements of the functional specifications of the IMO, the ECDIS must record and recover some of the key elements of the voyage required to record the history of the piloting and used enc and other information for the last 12 hours of the voyage. For this purpose shall be continuous recording at intervals not greater than 1 min the following elements:
1) Position, course and speed of the vessel for redesign of the program itinerary and the recovery of the detailed historic piloting.
2) Detailed information used, number of bay, year of issue, official corrections.

## Slide 25: WECDIS (Warship Electronic Chart Display and Information Systems)
Advanced form of ECDIS are the Warship Electronic Chart Display and Information Systems (WECDIS) which combines a system of shipping functions ECDIS systems and part of the Information Center a modern Battleship. The main functions of the WECDIS determined by each country according to its own national needs. The NATO (North Atlantic Treaty Organization), has adopted the standardization agreements "STANAG 4564 - Standard for Warship Electronic Chart Display and Information System (WECDIS)" in which shall be as follows: (I) The Essential (mandatory) operational capabilities of a simple system WECDIS (ii) Additional (recommended) business potential of a system WECDIS.

## Slide 26: WECDIS (Warship Electronic Chart Display and Information Systems)

## Slide 27: WECDIS (Warship Electronic Chart Display and Information Systems)
The Standardization Agreement NATO STANAG 4564 Ed.2 specifies the types of digital data used in the WECDIS, known as the WECDIS Data Products (WDP), which are defined groups data containing all the related information to support the functions of the WECDIS. The categories of digital data WDP is the following:
A. Core Navigational Information - CNI: Include all necessary digital data in vector format (vector) required for safe navigation. Such information is essentially the Electronic Navigational’s (ENCs) and/or Digital Navigation Charts (DNCs).
B. Auxiliary Navigation Information-ANI: Include all necessary digital data needed to conduct safe navigation feature that can be used as reserve of the Cni Information or where it is not available CNI information. Essentially the ANI information other electronic charts vector such as Admiralty Raster Chart Service (ARCS)
C. In addition Military Data-AML: In the case of digital files Geospatial (Geospatial information manufactured specifically for the support of seafarers.

## Slide 28: Operational Opportunities on WECDIS
A. Essential Business Features: Covering all the main shipping requirements of the ECDIS and optional features such as interface with radar/ARPA (Automatic Radar Plotting Aid), Automatic Identification System Ships (AIS) & Navigational Telex (Navtex receivers), providing data weather and tide, plot hazardous areas for Navigation, interface with systems GMDSS & INMARSAT etc. Provide basic business functions such as the presentation of data Automatic recognition of warships (Warship Automatic Identification System-WAIS).
B. Additional Operational Capacity: WECDIS systems to support specialized maritime companies. Supplied with a wide range of digital data, providing specialized features to support business needs, missions of each type of warships (specialized functions WECDIS to support Amphibians enterprises.

## Slide 29: Additional Military System Data on WECDIS (Additional Military Layers-AML)
Nato member states have adopted product specifications AML, while another product is under preparation.
The approved types of AML products are the following:
Products AML vector - Vector AML
- Contour Line Bathymetry (CLB)
- Environment, Seabed and Beach (ESB)
- Large Objects Nets - Large Bottom Objects (LBO)
- Parent Shipping Information and Services - Maritime Foundation and Facilities (MFF)
- Routes, areas and limits - Routes, Areas and Limits (RAL)
- Small Objects Depth, Small Bottom Objects (SBO) (UKHO currently produces the V1.0)
Products AML interlaced form - Gridded AML
- Integrated Water Column - Integrated Water Column (IWC)
-Sediments, the environment and the sea floor and coastlines Interlaced Form Gridded Sediment, Environment, Seabed and Beach (GS ESB).

## Slide 30: Conclusion
Benefits:
• Reduced workload for the navigator
• Navigation in real time increasing situational awareness in combination with proper lookout
• Automatic route monitoring (warnings and indications of hazards to the operator, in time arrivals)
• Automatic track control (reduces bunker costs), if ECDIS is connected to the autopilot
• Prediction of special maneuvers (predicted path, trial maneuvers, docking mode)
• Availability of a chart during the night without night vision loss
• Access to additional information resources

## Slide 31: Conclusion
Disadvantages:
• Too much information on the screen may cause clutter and can be distracting
• Submenus can be very complex
• The size of chart displayed on the screen monitor is very much reduced compared with the paper chart
• Some symbols may be misinterpreted due to unfamiliarity
• Automatic plotting of position can lead to complacency concerning the vessel’s position and proximity to dangers.