## Slide 1: INTERDEPARTMENTAL OF POSTGRADUATE STUDIES PROGRAM “INFORMATICS AND COMPUTATIONAL BIOMEDICINE” FLOW: “INFORMATICS” COURSE: SHIPPING INFORMATICS FINAL WORK GLOBAL NAVIGATION SATELLITE SYSTEMS – GNSS IN SHIPPING
Angelis Evangelos - MYloni Vasiliki
Teacher / SUPERVISOR : FILIPPOPOULOS IOANNIS
LAMIA, JANUARY 2018
UNIVERSITY OF THESSALY
SCHOOL OF POSITIVE SCIENCES

## Slide 2
WHAT WE WILL BE PRESENTED
HISTORICAL RECURSION
SATELLITE SYSTEMS OF DETERMINATION FOR POSITION, NAVIGATION AND TIME
BASIC PRINCIPLES OF OPERATION OF GNSS
GPS,
GLONASS, GALILEO, BEIDOU
SATELLITE SIGNALS
BASIC PARTS OF GNSS

## Slide 3
WHAT WE WILL BE PRESENTED
METHODS OF SATELLITE DETERMINATION OF POSITION
SATELLITE TRAJECTORIES OF GNSS SYSTEMS
GNSS SATELLITE RECEIVERS
MARITIME USES OF GNSS
OPERATING CYCLE
BASIC UNITS

## Slide 4: HISTORICAL RECURSION
1957 Sputnik-1 satellite launch.
High precision satellite positioning system for Navy.
1960 Satellite navigation systems.
Military uses initially.
Uses of navigation, aviation, geodesy etc., until the end of 1990.
1980 Second generation satellite navigation systems.
Navsat/Transit of US Tsikada of the Soviet
Union
Position, Navigation and Time Systems – (PΝΤ)
GPS of US
Glonass of the
Soviet Union

## Slide 5: SATELLITE SYSTEMS OF DETERMINATION FOR POSITION, NAVIGATION AND TIME
Various categories:
Global Navigation Satelite System – GNSS
GPS, Glonass, Galileo, Beidou initially as a regional one.
Regional Navigation Satellite Systems – RNSS
QZSS of Japan, IRNSS of India.
Satellite Based Augmentation Systems – SBAS
European EGNOS system, WAAAS for US-Canada,
MSAS of Japan, GAGAN of India.

## Slide 6: BASIC PRINCIPLES OF OPERATION OF GNSS
Determination of position in GNSS
Measuring receiver distances from at least four satellites.
In particular, the position of the receiver is determined in the intersection of four spherical surfaces, which have centers of the positions of the satellites and the radii measured at all times by the receiver.

## Slide 7: BASIC PARTS OF A GLOBAL GNSS SATELLITE NAVIGATION SYSTEM
The satellite segment System satellites.
The Control Department Network of earth stations.
The users section All system receivers that are used in a wide range of civilian and military applications.

## Slide 8: METHODS OF SATELLITE DETERMINATION OF POSITION
Maritime (kinematic) positioning.
Static positioning.
Differential positioning.
Real time Kinematic determination of centimeter accuracy (RTK).
Determination of real-time centimeter precision position (Wide Area RTK - WARTK).

## Slide 9: SATELLITE SIGNALS
Coded radio signals.
Categories of signals:
  1. Continuous sinusoidal signal Carrier wave
2. Digital signal with pseudo-random sequence code - pulses (chips)
3. Digital signal Maritime Message - pulses (bits)

## Slide 10: SATELLITE TRAJECTORIES OF GNSS SYSTEMS
Types of satellite orbits
Height of trajectory
The angle of inclination of the orbital plane to the plane of Ecuador
The shape of the track (circular or elliptical)
The rotation period

## Slide 11: SATELLITE TRAJECTORIES OF GNSS SYSTEMS
The determination of the location of the satellites is based on the three Kepler Laws.
Deviations of the actual satellite trajectories are provided in satellite newspapers.

## Slide 12: GPS
To determine the location (stigma) of the satellite receiver, the GPS satellites emit the following three coded signals:
Pseudo-random sequence code of common precision
(Coarse Acquisition Code – C/A).
Pseudo-random sequence code of high precision (Precision Code – P).
Data code (D – Code) or maritime message.

## Slide 13: DEPARTMENTS OF GPS
Space segment operates with 27 satellites in total (24 basics and 3 backup).
GPS ground control:
1) A primary control station.
2) Five additional ground monitoring stations.
GPS System Users Section - Services Provided.

## Slide 14: GLONASS
The satellite signals of Glonass Carrier frequencies configured with pseudo-random sequence codes and a maritime message as in GPS.
Carrier frequencies
Pseudo-random sequence codes C/A and P.
G1 (1602 MHz), G2(1246 MHZ),
G3 (1204,704MHz)

## Slide 15: DEPARTMENTS OF GLONASS
Space segment operates with 24 satellites in total (21 basics and 3 backup).
Glonass ground control:
1) A primary control station
It is divided into two functional sections:
a) Central synchronizer
b) Phase control system
2) Four ground-based monitoring stations
Glonass System Users Section - Services Provided.

## Slide 16: GALILEO
The satellite signals of the Galileo system Wider range of frequencies compared to GPS and other GNSS systems.
Different carrier frequencies, configured as in the case of GPS and Glonass systems.
Pseudo-random series codes
and maritime message.

## Slide 17: DEPARTMENTS OF GALILEO
Space segment operates with 30 satellites in total
(27 basics and 3 backup by 2020).
Galileo ground control:
1) Galileo Control System – GCS:
a) Network of five stations of Telemetry Traching and Control – TT&C.
b) Two Centers of Ground Control – GCC.
2) Galileo Mission System – GMS
uses a global network of 40 Galileo Sensor Stations – GSS.
Galileo System Users Section - Services Provided.

## Slide 18: BEIDOU
BeiDou satellite signals Six different carrier frequencies.
These signals are configured with pseudo-random sequence and maritime message codes.
Its three emission frequencies coincide with the frequencies of Galileo.

## Slide 19: DEPARTMENTS OF BEIDOU
Space segment operates with
35 satellites in total.
BeiDou's ground control department:
1) One Master Control Station.
2) Two Upload Stations.
3) 30 basics Monitor Stations.
BeiDou System Users Section - Services Provided.

## Slide 20: GNSS SATELLITE RECEIVERS
Today, a GNSS receiver can practically consist of a limited number of integrated circuits and have very small dimensions and weight, unlike the very bulky satellite navigation receivers of the first satellite navigation systems of the 1960’s.

## Slide 21: OPERATION CYCLE OF A GNSS RECEIVER
Recognizing satellites in its area, measuring distances and synchronizing with them.
Receiving a maritime message and calculating exact position of satellites.
Use distances (at least four) of known satellite positions to calculate the receiver location and calculation of the speed of the receiver by exploiting the Doppler phenomenon.
Converting the calculated position of the receiver to longitude, width and height based on a geodetic reference system (usually WGS 84).

## Slide 22: BASIC UNITS OF A GNSS RECEIVER
Preamplified antenna.
  Categories
1) Monopole
2) Quadrifilar
3) Microstrip
4) Spiral
Unit for converting the received radio frequency to the intermediate frequency (RF / IF unit).
Digital signal processing unit or digital correlation unit => It has evolved into GNSS software receivers.
Multi-directional, even the weakest signals possible
GNSS Maritime Receiver (GPS, Glonass, Galileo,
BeiDou, WASS, EGNOS), in which antenna and satellite receiver are integrated into one unit.

## Slide 23: MARITIME USES OF GNSS SYSTEMS
Immediate and continuous determination of the position of the ship in real time with precision.
Perform a precision navigation such as:
1) The registration on the receiver of several shipping routes, defined
by successive change of course points or way points
(e.g. Anchorage Safety, Keeping Distances etc.).
2) The provision during the voyage of indications of distance from a
way point and the course to be observed for arrival at that point.

## Slide 24: MARITIME USES OF GNSS SYSTEMS
Navigation support capabilities with GPS are increasing rapidly when the GPS receiver is used for its net-centered connection with other electronic naval instruments and systems, such as ECDIS and AIS, the Marine Radar / ARPA, the sonar device, the log and the integrated navigation systems and the integrated bridge systems.

## Slide 25: MARITIME USES OF GNSS SYSTEMS
Transfer of way points from computer to receiver and vice versa.
Warning that the boat is out of the planned route at a distance greater than the user defined maximum allowable deviation (off track limit).
Warning that the boat is approaching the next change or destination point depending on the user defined distance from that point.
Anchorage safety warning when the vessel has been dropped from the anchoring position at a distance greater than that specified by the user.

## Slide 26: MARITIME USES OF GNSS SYSTEMS
Identification / avoidance of individual hazards (warning when the position of the vessel is less than the user defined safety distance from a way point).
Indications of reliability and provided stigma accuracy, usually with the Geometric Dilution of Precision GDOP, PDOP, HDOP, and VDOP parameters.
Selection of satellites to be used or not to be taken into account for the determination of the position.

## Slide 27: REFERENCES
http://artemis.cslab.ntua.gr/el_thesis/artemis.ntua.ece/DT2012-0122/DT2012-0122.pdf
https://el.wikipedia.org/wiki/Global_Positioning_System
http://erodios.it.teithe.gr/BlindNav/GPS/GPS.htm
https://www.gps.gov/systems/gps/modernization/
https://www.ncbi.nlm.nih.gov/pmc/articles/PMC4321187/
http://users.sch.gr/mppapado/downloads/GPS.pdf
https://www.princeton.edu/~alaink/Orf467F07/GNSS.pdf
http://multimedia.biol.uoa.gr/MDE-AKTINOBOLIES/FEK399-syxnothtes%20genika.pdf
https://eclass.teicrete.gr/modules/document/file.php/TD103/%CE%A0%CE%95%CE%A1%CE%99%CE%95%CE%A7%CE%9F%CE%9C%CE%95%CE%9D%CE%9F/%CE%A3%CE%97%CE%9C%CE%95%CE%99%CE%A9%CE%A3%CE%95%CE%99%CE%A3/K.7-/7.pdf

## Slide 28: REFERENCES
http://w3.uch.edu.tw/ccchang50/ebook_introduction%20to%20gps.pdf
http://www.navipedia.net/index.php/Main_Page
http://hmga.gr/storehouse/word-acrobat/GPS.pdf
GLONASS-ICD (2008). GLONASS Interface Control Document. Version 5.1, 2008,
Available from http://gauss.gge.unb.ca/GLONASS.ICD.pdf
Aerospace Corporation, (2003). GPS Primer: A Student Guide to the Global Positioning System. Los Angeles, USA. Available at :
https://florida.theorangegrove.org/og/file/9129db88-b76c-0c3b-2149- 344ce701f190/1/GPS-Primer.pdf
Betz, J. W. (2002). Binary offset carrier modulation for radio navigation. Navigation, 48 (4): 227-246.
doi: 10.1002/j.2161-4296.2001.tb00247.x
Feng, Y (2003), Combined Galileo and GPS: A Technical Perspective. Journal of Global Positioning Systems, 2 (1): 67-72.
Cojocaru.S. et. al. (2009). “GPS-Glonass-Galileo: A Dynamical Comparison”. Journal of Navigation, 62, pp 135-150. doi:10.1017/S0373463308004980.
Euler H. J. (2005): Reference Station Network Information Distribution, IAG Working Group 4.5.1: Network RTK. Available at: http://www.wasoft.de/e/iagwg451/euler/euler.html

## Slide 29: REFERENCES
Commission of the European Communities, The World Radiocommunication Conference 2003 (WRC-03), Brussels. Available at:
http://eur-lex.europa.eu/LexUriServ/LexUriServ.do?uri=COM:2003:0183:FIN:EN:PDF
https://repository.kallipos.gr/bitstream/11419/2712/5/00_master_document.pdf
Hofmann-Wellenhof, B., Lichtenegger, H. and Wasle, E. (2008). GNSS-global navigation satellite systems. Wien: Springer. Available at: https://nguyenduyliemgis.files.wordpress.com/2014/09/gnss-global-navigation-satellite-systems-gps-glonass-galileo-and-more-2008.pdf
Januszewski, J. (2014). “GNSS Receivers, Their Features, User Environment And Applications”. Annual of Navigation,21(1). Available at: yadda.icm.edu.pl/.../Annual_Januszewski_21.pdf