## Slide 1: Telemedicine In Maritime
Christodoulou Irene - Karagianni Anastasia

## Slide 2: Introduction
The diagnosis of diseases and illnesses, as well as the treatment of sufferers and injured at sea, continues to be a challenge for Maritime and Naval Medicine in particular.
In the cases where there is no doctor or nursing staff on board, one member of staff is responsible for providing medical care to other members when required.
  The responsible person should be based on :
    any medical / health education available in existing written instructions
    information and manuals
    radio-medical and telemedicine advice and instructions that can be obtained from the land
These capabilities will enable him to use both the medical equipment and the medical equipment on board.

## Slide 3: Telemedicine
The provision of medical care by all health professionals, where distance is a critical factor, using information and communication technologies to exchange valid information, to diagnose, treatment and prevention of diseases, research and evaluation, as well as the continuous training of health functions, but also for all those that are in the field of upgrading the health services of the community anion .
  One of the needs of telemedicine is also shipping.
Telemedicine in Maritime
Adaption of telemedicine technology at sea, using digital libraries :
  Distribution of medical information to care provider from any remote location
Implementation of the Marine Virtual Hospital with the task of creating and assisting a digital Health Science Library in order to make the internet a useful medical tool for Marine Medical Care as well as a health promotion tool for seafarers .
Thanks to assessors capabilities, a rapid assessment of the patient's condition or the injured person can be made in order to obtain a timely and valid decision to move when it is required or to stay on board and receive the appropriate treatment, following a doctor's advice from the land.

## Slide 4: Technological Factors Contributing to the Application of Technology in Healthcare and Ship Surveillance
Right distribution of information:
  Directly distribution of information between patients and care providers on ships
  Condition: the right data management
The medical data of telemedicine services are classified into three categories, depending on their type:
  Data:
    Static( such as a patient's medical records)
    Dynamic (such as the transfer of vital signs, cardiac types, blood pressure, etc.)
    Applications:
      Telemetry applications(ability to monitor the physiological functions of patients from a remote location).
      Information services(hospitals and private doctors exchange information, such as records relating to the evolution of the health of patients and used diagnostic methods
  Audio( communication and advice between two doctors using the phone).
  Image( for example x-rays, or application is for tele-radiology ).

## Slide 5: Programs-Telemedicine Systems for Ships
NIVEMES
MERMAID
TELE-IASIS
WETS
GALENOS
MEDASHIP
GLAROS

## Slide 6: NIVEMES (Network of integrated vertical medical services)
This network is made up of Medical Organizations (Hospitals, Medical Centers) connected to a unified "virtual organization" of health services.
ATKOSoft Software
Supports diagnosis based not only on primary data but also on the patient's complete medical history,
  the substantiated exchange of requests / replies and teleconferencing
  the development of security mechanisms that ensure medical confidentiality.
The quality of service provision to remote and mobile population groups has been greatly upgraded.
The chances of accurate remote diagnosis have increased.
Reduced unnecessary displacements in central hospitals.

## Slide 7: MERMAID (Medical Emergency Aid Through Telematics)
Based on the basis of medical assistance and advice on the safety of those working at sea and ships and naval bases.
The communication technologies of the project can be divided into two main points:
  transmission media (Fiber Optics, Copper Cables, Communication Satellites, Radio Cell Technologies, Wireless Networks, Radio to Navigation) and
  networking systems (Asynchronous mode of transmission, B-L.S.D.N. for ATM reference protocol model, ATM and narrowband services, Internet).
MERMAID's telecommunication software must include:
  A medical record system useful for recording the patient's history.
An Assistance option that would be offered through a multimedia application to quickly find help in the form of medical advice.
A database of all data on medicines and medical equipment.

## Slide 8
The Ship Message System (SeaVessels-SVs) initially communicates with a Ground Central Station (G.C.S) located in Greece (BIOTTRAST).
The G.C.S determines which of the Medical Care Centers (M.C.Cs) can handle the call for help made by S.V.
The election of the M.C.C depends on the position of the ship, the language spoken by the passengers on it or even the suitability of the medical center itself for the particular case.
MERMAID System Architecture

## Slide 9: TELE-IASIS
Goal : the continuously monitoring of patients' images in real-time and their transmission not only by wireless, which can be used on ships but also by wired communication networks, at the base station which is located in the large hospital coordination center .
Allow a real-time transmission of critical bio-signals such as electrocardiography, blood pressure, oxygenation, pulse, temperature, and images at the hospital's coordination center, giving to doctors a complete view of the patient's condition.
Flexible , reliable, innovate, safe, easy
Possibility of using all telecommunication networks, thus developing a wider range of applications.
Possibility of interconnecting the system with Hospital Information Systems for access to additional information concerning the Patient.
Connection to the most important physiological parameter measuring devices. System development based on commonly accepted IEC / ISO9126 quality standards.
Use a TCP / IP protocol that allows secure and accurate data transmission. Small-sized device, light, ergonomic, with friendly working environment, even for beginners.
Portable device with 3 hours of continuous operation.

## Slide 10: WETS (Worldwide Emergency Telemedicine Service)
Provides support to any mobile unit in case of emergency medical emergency on land, sea and air, which is achieved through:
  the use of different communication links (i.e. GSM, Satellite, Radio, ISDN),
  the use of positioning system (i.e. GPS) ,
  the transmission of vital signs and images
  the access to relevant clinical information
  using an on-board decision support tools (i.e. Multimedia Medical Guide),
  the access to remote medical expertise (i.e. healthcare referring centers).

## Slide 11: GALENOS (Generic Advanced Low-cost trans-European Network Over Satellite)
A Low-cost trans-European satellite network, dedicated to telemedicine applications, has been implemented in 14 clinics, six (6) countries.
Through satellite (WoTeSa).
Communication software: WinVicos.
In addition to receiving digital images for medical education, they are trained using state-of-the-art communication, video and computer technologies required for collaborative work on a network of distributed medical information.
Such distributed medical networks provide intelligence to the competent network and allow e.g. local doctors or local hospitals facing unexpected results in order to get online advice from the nearest academic hospital (intraoperative radiological televising).

## Slide 12
Interactive eLearning
Intraoperative Radiological

## Slide 13: MEDASHIP (Medical Assistance for Ships)
Supplies integrated solutions for medical consultations on-board of ships
The satellite-based telemedicine services address both passenger ships and merchant vessels
Provide to passengers and crew members an effective medical assistance in cases of emergency and in all those cases where the on board medical staff requires second opinion.
During the validation phase the service was tested on board of three ships with the possibility to have it connected to three land medical centers
Network linking MEDASHIP with specially equipped Mediterranean ships with the special equipped ships from Mediterranean with three reference hospitals in Athens ,Genova, Berlin

## Slide 14
In addition to the standard medical equipment aboard the ships, two video cameras, an electrocardiograph (ECG) and an ultrasound (US) equipment are used.
Τelemedical services
  Teleconsultation (a live camera on-board of the ship can be used to transmit the image of the doctor who is leading the examination on-board of the ship or the image of the patient when being questioned by the land-based expert).
  Electrocardiography (connected to WoTeSa on board the ship and be controlled by the physician from this workstation).
  Telesonography (not only still images can be transferred but also live ultrasound investigations can be transmitted at 500-700 kbps)
Reduction of cost:
  The removal of a passenger in the Carribean can cost up to $ 11.000 and the cost for hospitalisation can range from 500-1000 € per day.

## Slide 15: GLAROS
Provides possibilities for managing and sending the patient's electronic medical record as well as the possibility of videoconference between doctors.
  The data is stored in a database and displayed by patient and visit as the user can have directly access to each patient's data.
  Pressing only a key, the user can digitize images and radiographs and enter them into the system.
Possibility of conference call between doctors
Supports all the widespread types of telecommunication connections such as analogue PSTN, ISDN Digital Telephony, Mobile Telephony, Satellite Telephony and ADSL.
It is complete and easy to use because it was designed by doctors of various specialties.

## Slide 16: GMDSS (Global Maritime Distress and Safety System)
Interconnection of various systems (NAVTEX and Safety-NET navigation information transmission systems and INMARSAT, COSPAS-SARSAT, Galileo).
  Immediate activation of search, transmission, and rescue services by making a one-touch risk call only at the touch of a button.
  Providing ships with high communication capabilities.
Most important of the new communications capabilities of the GMDSS system are:
  Automatic and immediate reception of navigation safety information.
  Radiotelephony capable of direct two-way voice communication "ship-to-shore, ship-to-ship" and "ship-to-ship".
  Radiotelegraphy
  Digital Selective Calling DSC (Digital Selective Calling).
    used solely for dialing (emergency alarms in conventional communications)

## Slide 17
Group Call EGC (Enhanced Group Calling)
  Information is transmitted from shore to shore by:
Selection of ships belonging to a specific flag, regardless of the area in the Fleet-Net service(A)
Α
Selection of ships located in a specific geographical area(B)
Β

## Slide 18: Activating research and rescue procedure of GMDSS includes automatic update of adjacent ships, coastal stations and Rescue Coordinating Centers (RCC).

## Slide 19
The activation of search and rescue services is carried out with several terrestrial and satellite means, such as:
  Emergency signal transmission by GMDSS special transceivers.
  Activation of Emergency Position Radar Beacon-EPIRB (Figure 1)
  Activation of the Search and Rescue Radar Transponder-SART. (Figure 2)
Figure 1 1
Figure 2

## Slide 20: Maritime Telemedicine Solution (MTS)
Offers remote examinations and on-line diagnostics services on board.
Main advantage : solutions cost less in both money and time.
Overcomes clinically, providing excellent results in patient diagnosis and creating a greater sense of moral satisfaction and safety among crew members.
Provides a "safety zone" that can both relieve captain and shipowners of further concerns when dealing with sensitive medical cases.

## Slide 21: Conclusion
In conclusion, by pointing out that the value of human life is invaluable, telemedicine is the only dynamically evolving high-level medical care in patients who have no way of accessing Health Units at this level, such as marines and ship passengers.
However, the high cost of satellite telecoms remains a problem, although the equivalent of wired is significantly reduced.
Health care providers are responsible for monitoring and updating the developments in telemedicine.
Although it is the ideal solution for patients who have no other access to High-Level Health Service Units, but in no case can substitute the clinical practice of medicine next to his bed sick.
  the interpersonal relationship and the mental contact developed between the patient and the doctor cannot be substituted by screens and wires.

## Slide 22
Thank you
Christodoulou Irene - Karagianni Anastasia