## Slide 1: Minimizing Waiting Time at Intermediate Nodes for Intercity Public Bus Transportation
Saharidis G.K.D.
Dimitropoulos Ch.
Skordilis E.
ΠΑΝΕΠΙΣΤΗΜΙΟ ΘΕΣΣΑΛΙΑΣ

## Slide 2: Introduction
The purpose of this research is to create a suitable timetable for intercity buses, departing from various nodes of the network, such that the total waiting time of passengers at intermediate nodes is minimized.

## Slide 3: Description of the problem
By using the current infrastructure of the public bus companies in Greece (dubbed KTEL), we tried to reform the bus schedule, for better service of passengers who use intermediate nodes to reach their destination.
In many cases, the waiting time at these nodes is very long. The reason for this is that there are interconnections of various itineraries, which increments the difficulty of a suitable time schedule.

## Slide 4: Formulation of the problem
The problem is formulated as a mixed integer linear program.
The objective function is the minimization of the sum of waiting times for every intermediate node of the network

## Slide 5: Formulation of the problem
Assumptions:
Steady travel time between nodes
Steady number of itineraries (routes) between connected nodes
Sufficient parking space in bus terminals (no bottleneck)
Generally, parameters describing the problem are considered steady

## Slide 6: Decision variables
The departure time of every bus ()
The waiting time at an intermediate node ()
A binary variable that defines the combination of routes to and from an intermediate node as active or inactive ()

## Slide 7: Decision variables
The time difference between the bus departure and a high priority time (will be used as penalty factor) ()
A binary variable that defines the number of buses affected by the high priority time ()

## Slide 8: Illustration of the problem
Το σχήμα περιλαμβάνει
3 παράλληλες γραμμές
που αναπαριστούν τους
κόμβους αναχώρησης, άφιξης
και τον ενδιάμεσο. Το χρησιμοποιούμε
για να δείξουμε πως υπολογίζουμε
τον χρόνο αναμονής στον ενδιάμεσο.

## Slide 9: Sets, Parameters

## Slide 10: Sets, Parameters

## Slide 11: Constraints
Constraint (1) defines the combination of routes to and from an intermediate node as active or inactive, based on whether the bus from the intermediate node has already left or not

## Slide 12: Constraints
Constraint (2) calculates the waiting time between the arrival on each intermediate node and the first two available departing routes from that node towards the destination node.

## Slide 13: Constraints
Constraint (3) assures that a bus departing from any node will return to this node before and after a certain time

## Slide 14: Constraints
Constraint (4) assures that each bus departs after another.
Constraint (5) defines the time window in which a bus must depart

## Slide 15: Extensions
Furthermore, an extension regarding high priority times is introduced. By using this extension bus departures are gravitated towards certain times.

## Slide 16: Extensions
Constraints (7) and (8) calculates the time difference between the departing time of a route and the time where a high passenger demand occurs.
Constraint (9) defines the number of buses affected by these high priority times.

## Slide 17: Objective function
Minimization of the waiting time for all available buses departing from the intermediate node
Using the penalty factor :

## Slide 18: Case study
The formulation was applied to the intercity bus network of the island of Crete.
Numerical data for Crete network:
  122 nodes total.
  13 of these nodes considered intermediate.
  Number of routes between nodes varies from 2 to 25.

## Slide 19: Case study
We will examine three different cases:
Case 1 : Existing bus timetable (benchmark)
Case 2 : Minimizing waiting time without penalty factor
Case 3 : Minimizing waiting time with penalty factor to better approach the existing bus timetables

## Slide 20
For the penalty factor we introduced five high priority times, each corresponding to five time zones
330
540
750
960
1170
1380
Minute of the day:
435
645
855
1065
1275
Zone 1
Zone 2
Zone 3
Zone 4
Zone 5
Case study
High Priority Time:

## Slide 21: Case study
For each time zone, the number of buses affected by the high priority time was set by the number of buses departing, based on the existing bus timetable
This also applies to the weight factor of the penalty cost in the objective function

## Slide 22: Results
 | Total Waiting Time | (%)* | Number of Active Routes | (%)* | Average Waiting Time | (%)*
Case 1 | 1,994,385 | - | 33051 | - | 60 | -
Case 2 | 493,924 | 75.2 | 19361 | 41.4 | 25 | 58.3
Case 3 | 925,444 | 53.5 | 25565 | 22.6 | 36 | 40.0
*Percentage of decrease over existing timetable (Case 1).

## Slide 23: Results
Distribution of waiting times :
Distribution of itineraries :

## Slide 24: Conclusions
For all the examined cases there is a clear reduction of the waiting times
The use of a penalty factor (Case 3)results in an increased waiting time compared to not using it (Case 2)
However, it is greatly reduced compare to the existing bus timetable
Using of a penalty factor (Case 3) leads to timetable more suitable for realistic cases, giving passengers more choices considering their departure from intermediate nodes

## Slide 25: References
Steer Davies Gleave. Study of passenger transport by coach. Publication TREN/E1/409-2007. European Commission, 2009.
Ceder, A, Golany B, Tal O. (2001) Creating Bus Timetables with Maximal Synchronization. Transportation Research Part A. 35:913-928.
Eranki, A. “A model to create bus timetables to attain maximum synchronization considering waiting times at transfer stops”. Master’s thesis. Department of Industrial and Management Systems Engineering, University of South Florida, 2004.
Ibarra-Rojas, O. J., and Y. A. Rios-Solis. “Synchronization of bus timetabling”. Transportation Research Part B, Vol. 46, 2012, pp. 599-614.
Hall R., Dessouky M. and Lu Q. “Optimal Holding Times at Transfer Stations”. Computer and Industrial Engineering. Vol. 40, 2001, pp. 379-397.
Bussieck M. R., Winter T., and Zimmermann U. T. “Discrete Optimization in public rail transport”. Mathematical Programming. Vol. 79, Issue 1-3, 1997, pp. 415-444.
Goverde R. M. P. “Synchronization Control of Scheduled Train Services to Minimize Passenger Waiting Time”. Transport, Infrastructure and Logistics, Proceedings 4th TRAIL Congress, 1998.
Chen D. and Wu K. “Research on Optimization Model and Algorithm of Initial Schedule of Intercity Passenger Trains based on Fuzzy Sets”. Journal of Software, Vol. 7, No. 1, 2012, pp. 49-54.
Reinhardt L. B., Clausen T., and Pisinger D. “Synchronized dial-a-ride transportation of disabled passengers at airports”. European Journal of Operational Research. Vol. 225, 2013, pp. 106-117.
Wong R. C. W., Yuen T. W. Y., Fung K. W. and Leung J. M. Y. “Optimizing Timetable Synchronization for Rail Mass Transit”, Transportation Science, Vol. 42, No. 1, 2008, pp. 57-69.